## Slide 1
Overall research context
Cooperative Automated Vehicles (CAVs) advantages address many areas: safety with accident reduction; health while improving passengers comfort; transportation time since it reduces road congestion; ecology with fuel efficiency among other advantages.
Among the objectives of the Ph.D thesis, addressing the on-ramp merging on highway complexity. In fact, the CAVs permit with the help of a
flexible formation modeling and control and a safe motion synchronization to envision a cooperative merging strategy.
(a)
Scenario study: cooperative on-ramp merging
Cooperative merging strategy
Decision making level: decide on a safe and efficient passing sequence of the CAVs through the merging zone (cf. Figure 1).
Global planning level: decide on the global path of the CAVs w.r.t. their initial position and their destination, the road geometry, etc.
Local planning level: decide on the local trajectory of the CAVs w.r.t. their passing sequence and their reference global path.
Cooperative on-ramp merging for CAVs
(a): T=0s, initial configuration: the vehicles V1
and V2 are in the main line. V3 aims to merge
into the main line. The three vehicles are part
of a triangular formation.
(b): T=2s, reconfiguration phase: V3 enters the merging zone. A reconfiguration from a triangular shape toward a linear one is being performed.
(c): T=4.2s, reconfiguration phase: the merging vehicle merges into the main line between V1 and V2, while ensuring the respect of the minimum safety distance .
(d): T=7s, platoon formation: the three vehicles navigate through the main line in a linear formation.
Perspectives
Include vehicle’s dynamics on the proposed solution.
Implement the cooperative merging strategy in the laboratory’s vehicles.
Safe and Smooth On-ramp Merging on Highway Strategy for Cooperative Automated Vehicles
Lyes Saidi1, Lounis Adouane2 and Reine Talj3
Laboratoire Heudiasyc, UMR CNRS 7253, Université de Technologie de Compiègne, France
Journées du Comité Technique Automatique et Transport Terrestre (CT ATT) 2022
Contacts: 1: Lyes.Saidi@hds.utc.fr 2: lounis.Adouane@hds.utc.fr 3: Reine.Talj@hds.utc.fr
Figure 3: Velocity and in-between distance profile of each vehicle
Figure 2: The overall architecture of the cooperative merging strategy
Road congestion
Due to unnecessary speed changes and inefficient traffic management.
Platoon navigation
Reference trajectory
Risky zone
Merging zone
Safety distance
CAV
Connected Automated Vehicle
Equipped with localization and perception modules along with V2V Communication.
CAV
CAV
CAV
CAV
Figure 1: On-ramp merging on highway
V1
V2
V3
(a)
(a)
(b)
(b)
(c)
(c)
(d)
(d)